## Slide 1: Greenlight Project Evaluation Community and Place Division
Nikit Nain
Presenter
Notes: <number>
Objective of the IMAP/Greenlight Project was to lead to improved movement and crossing experience for pedestrians.
The objective of this presentation, though, is to provide information on the evaluation findings of the Greenlight Projects.

## Slide 2: Scope of Greenlight Project
Notes: <number>
Small scale changes
24 pilot sites
Impacts on:
  260,000 residents
  420,000 workers
School site was control site at Chapel St/Alma Rd

## Slide 3: Changes to Signal Operation
Late introduction of green man
Auto introduction
Increased clearance time
PUFFIN (Pedestrian User Friendly Intelligent)
Total cost of treatments $171,500
Notes: <number>
PELICAN - Pedestrian Light Indicator Crossing
PUFFIN - Pedestrian user-friendly intelligent

## Slide 4: Challenges
Scarce number of sites per treatment type
Extended gap between pre and post intercept surveys
Changes in land uses, population and demographics
Direct information on near misses not captured
Lack of international research or similar studies
Notes: <number>
Scarce number. Total number of sites (20) and the mix of treatments implemented meant only 6-7 sites per treatment were available for assessment. This led to inconclusive results and inability to establish significant statistical correlation.
Extended Gap between surveys : Pre-implementation Dates (Video Data and Intercept Surveys – July/August 2007)
Post –implementation Dates (Video Data - April 2010, Intercept Surveys – March 2010) – could have led to changes in demographics and land use.
Near misses. Information on near misses was captured indirectly through survey responses. Proxies used to capture this information were
Non compliance
Reduced crossing speed
Feeling rushed
Treatments were implemented between August and September 2009.

## Slide 5: Late introduction of green man
Improved safety
  Instances of crossing on the ‘red man’ have reduced by 16%
  A 21% increase in feelings of increased safety
More comfortable crossing speed
  0.09 metres/second decrease in average crossing speeds
Increased wait time with less frequent phases
  waiting time has increased by 1.8 seconds
Average cost per site $2,500

Notes: <number>
Allows pedestrians be more visible to drivers as they enter into the crosswalk first
Proviso: Costs can vary depending on hardware upgrades.

## Slide 6: Auto introduction
No improvement to safety
  Instances of crossing on the ‘red man’ have reduced by 1%
  There has been a significant decrease (24%) in the proportion of respondents who feel safe at these intersections
More comfortable crossing speed
  0.03 metres/second decrease in average crossing speeds
Increased wait time with less frequent phases
  waiting time has decreased by 0.2 seconds
Average cost per site $1,400
?
Notes: <number>
Counterintuitive outcome: possibly because of lack of comparable waiting time data. It is possible that an external variable may be having a significant impact on pedestrian safety and comfort due to auto introduction.
Background noise (Also see challenges slide).
Site at Chapel St/Chatham St had a cost of $22,000
BUT Proviso: Costs can vary depending on hardware upgrades.

## Slide 7: Increased clearance time
Improved safety
  Instances of crossing against the ‘red man’ decreased by 2%
  A 24% increase in feelings of increased safety.
More comfortable crossing speed
  0.03metres/second decrease in average pedestrian crossing speeds.
Average cost per site $2,300

Notes: <number>

## Slide 8: PUFFIN
Improved safety
  Instances of crossing against the ‘red man’ decreased by 12%
More comfortable crossing speed
  0.03 metres/second decrease in average pedestrian crossing speeds.
Increased wait time with less frequent phases
  waiting time has increased by 5.5 seconds (the largest of all increases in wait times)
Average cost per site $30,000

?
Notes: <number>
PUFFIN’s are used primarily at mid block locations.
Pedestrian user-friendly intelligent
It is a demand responsive treatment
In addition to detecting people waiting to cross, it is also able to identify people still in the crossing and thus extend the clearance phase

## Slide 9: Overall findings
There is a significant effect of an increase in flashing red man ‘clearance time’ on decreasing the average walking speed of pedestrians.
The Greenlight treatments have led to an overall decrease in the number of people entering the crossings during the ‘red man’.
Notes: <number>

## Slide 10: Recommendations
Treatment Type | Key Recommendation
Late introduction of green man | Approach VicRoads to make this treatment type standard, for existing and proposed sites, in all areas of pedestrian priority.
Auto Introduction | Consider international context including expected benefits and revisit analysis
Increased Clearance Time | As for ‘Late introduction of green man’
PUFFIN | Request VicRoads to balance ped wait times and provide regular crossing opportunities.
Notes: <number>
Smart Roads speak about it for point 1

## Slide 11: Next steps for DOT
Work with VicRoads to convert these findings into revised policies and procedures to be applied at all signal sites within areas of pedestrian priority
Share the key findings of the Greenlight study with Councils, VicRoads, DPCD, DEECD and other divisions within DOT
Notes: <number>
Survey Design – (1) intercept surveys should focus on crossing as opposed to combining results over the whole intersection (2) to add richness to the data collected, surveys should capture perceived instances of near misses (3) greater sample size (was 625) (4) include ped line of sight/land use and dvpmt changes (5) survey design could get behavioural input to better understand ped behaviours (6)